## Slide 1
Wire Rope
Safety Factor

## Slide 2
Wire Rope Safety Factor
The Wire Rope Safety Factor is a measure of the margin of safety between the breaking strength of a wire rope and its working load limit (WLL). It is calculated by dividing the breaking strength of the wire rope by its working load limit. The safety factor is crucial in crane operations to ensure that the wire rope is not used at or near its maximum capacity, providing a margin of safety against potential overloading and reducing the risk of failure.
Formula:
Safety Factor = Breaking Strength / Working Load Limit
Breaking Strength and Working Load Limit (WLL): Breaking strength and working load limit are essential parameters provided by wire rope manufacturers:
Breaking Strength:
  The breaking strength is the maximum load a wire rope can withstand before breaking.
  Manufacturers determine breaking strength through rigorous testing.
  Breaking strength is usually specified in tons, pounds, or kilograms.
Working Load Limit (WLL):
  The working load limit is the maximum load that a wire rope is designed to handle in normal working conditions.
  WLL considers factors like safety, potential dynamic loading, and wear over time.
  It is specified by the manufacturer and is often expressed in tons, pounds,
  or kilograms.

## Slide 3
Let's consider a wire rope with a breaking strength of 100 tons and a working load limit of 20 tons.
Safety Factor = 100 tons / ​20 tons = 5
In this example, a safety factor of 5 means that the breaking strength of the wire rope is five times higher than its working load limit (WLL). It ensures that the wire rope is not used at its breaking strength, reducing the risk of failure during lifting operations.