## Slide 1: Differences Between HIRA (Hazard Identification and Risk Assessment) and JSA (Job Safety Analysis) Explained with Each Example

## Slide 2: 1. HIRA (Hazard Identification and Risk Assessment)
Definition: HIRA is a systematic approach to identifying all potential hazards in a workplace, evaluating the risks associated with those hazards, and determining control measures. It is typically broader in scope and covers all workplace hazards.

## Slide 3: HIRA Example: Construction Site Assessment Project: Residential Building Construction Scope: Entire Construction Site
Activity | Hazard | Risk Level | Control Measures
Working at Heights | Falling from height | High | Install guardrails, use safety harnesses, conduct training.
Heavy Machinery Operation | Collision, tipping | Medium | Operator certification, clear signaling, regular maintenance.
Handling Hazardous Materials | Chemical burns, respiratory issues | High | Use PPE (gloves, masks), proper storage, safety data sheets.

## Slide 4
Summary: This HIRA provides an overall view of hazards at the construction site, classifying them by risk level and identifying control measures for each hazard category.

## Slide 5: 2. JSA (Job Safety Analysis)
Definition: JSA is a process focused specifically on individual tasks. It breaks down a job into specific steps, identifies hazards at each step, and determines control measures to prevent incidents. JSA is more detailed in its analysis of how a particular task is performed and how risks can be minimized.

## Slide 6: JSA Example: Task-Specific Analysis for Installing Scaffolding Project: Residential Building Construction Task: Installing Scaffolding
Step | Hazard | Risk Level | Control Measures
1. Transporting Materials | Back injuries, slips, trips | Medium | Use proper lifting techniques, ensure clear pathways.
2. Assembling Scaffolding | Falls, instability | High | Wear harnesses, check stability, secure base.
3. Securing Bolts and Rails | Pinched fingers, equipment failure | Medium | Use gloves, double-check bolts and connections.
4. Inspecting Scaffolding | Loose parts, structural failure | High | Conduct inspection checklist before use.

## Slide 7
Summary: This JSA focuses on a specific task—installing scaffolding—by breaking down each step, identifying potential hazards, and implementing step-by-step safety controls.